#### The complex for moving targets

A brief technical descriptions

1. Table of Contents.

- Table of Contents.

- Appointment.

- Product composition.

- Technical data.

2.   Appointment.

The system is designed for delivery of target on predetermined distance, and turns the target face or edge.

3. Product composition.

3.1.Carriage

- The case is made of stainless steel with a thickness of three millimeters, and enhanced frontal armor.

- Support frame - made of stainless steel with a thickness of 4mm

- Drive of motion.

- Drive for target rotation.

- Battery.

- Control unit.

- Radio link.

3.2. Unit control panel.

- Console.

- Radio link.

3.3. Unit charging

1)  The power supply control unit..

2)  Сharging.

3)  Unit pin terminal.

4. Dimensions

5.   Unit pin terminal.

Mass:  ~20 kilo.

Working temperature:  +5 … +40°C.

Parameters voltage for charging:  110 – 220 volt.

Power consumption:  During charging the carriage on terminal maximum  30 watt, while waiting 10 watt.

The maximum length of the rail:  200 m.

Voltage Power of Carriage:  24 В volt. DC.

Speed of movement of the carriage:  2,5-3,0 m / s.

Power reserve on a single charge for 10 hours of work:  ~4000 m.

The angle of rotation of the drive target:  90°.

Maximum torque of the drive target:  5 Nm.

The time of rotation of the target:  0,4-0,6 s.

6. Plans set the distance mark

7. Example of placing the complex in a room.